## Slide 1: SoC-based Architecture for Biomedical Signal Processing
Authors: R. Gutiérrez-Rivas, A. Hernández, J. J. García, W. Marnane.
Source:2015 37th Annual International Conference of the IEEE Engineering in Medicine and Biology Society (EMBC)
Presented by:
Progga Labani Howlader
Roll:1509035

## Slide 2: Overview
Background
Introduction
What is SOC Architecture
Detection of QRS complex
Implementation of QRS complex detector
Results
Conclusions
References
1

## Slide 3: Background
Figure 1: Heart.
18 million were attacked due to the coronary heart disease
7.2 million are stoke problem
Human heart rate activity can be electrically recorded in the (ECG) signal
ECG reveal a number of heart disorders
2

## Slide 4: Introduction
In biomedical signal processing, many algorithms focused on the noise reduction and eliminates artifacts existing in the signal.
Power consumption and computational complexity has been observed.
But SoC (System-on-Chip) architecture, based on a FPGA(Field-Programmable Gate Array)device, suitable for the implementation of biomedical signal(ECG signal)processing.
This architecture reduce number of resources , sensitivity , increase positive predictive value.
3

## Slide 5: What is SOC Architecture
Based on FPGA device
Proposed for implementing ECG signal processing algorithms.
Provides a logic area for real time solution.
Allows complex control tasks.
Xilinx Zynq device used to implement
4

## Slide 6: SOC Architecture(continued…)
Figure 2: General block diagram of SoC architecture
5

## Slide 7: Detection of QRS Complex
Figure 3:General block diagram of the proposed algorithm for the detection of QRS complex
Implementing a detection algorithm for QRS complex in ECG signal , thus the signal processing has been validated.
6

## Slide 8: Detection of QRS Complex(continued…)
A. Pre-processing stage:
use input ECG signal [x(n)] at sampling frequency, fs=360 Hz.
This input signal consists of minimum hardware resources.
B.QRS detection stage:
based on a dynamic threshold th(n)
amplitude depends on the ECG signal amplitude
controlled by a FSM with 3 States. 7

## Slide 9: Detection of QRS Complex(continued…)
Figure 4:State diagram of the FSM controlling the detection threshold th(n)
8

## Slide 10: Implementation of QRS complex detector
The QRS detection stage follow this block diagram
Figure 5:Block diagram of the proposed low-level peripheral
9

## Slide 11: Implementation of QRS complex detector(continued…)
Configurable filter:
provide enough flexibility.
Figure 6:Block diagram of the configurable FIR filter
10

## Slide 12: Implementation of QRS complex detector(continued…)
Moving average:
Figure 7:Block diagram of the moving average block
11

## Slide 13: Implementation of QRS complex detector
After the pre-processing stage , the resulting signal y(n)is analyzed by a finite state machine (FSM) which is the exponential function.
12

## Slide 14: Results
This table describes the word widths defined for SOC architecture.
13

## Slide 15: Results(continued….)
This table shows the resource consumption for the different elements in the system.
14

## Slide 16: Results(continued…..)
Sensitivity and positive predictive value is
15

## Slide 17: Conclusion
SoC Architecture presented for real-time implementation of biomedical signal processing algorithms.
This architecture has been validated through ECG signals with high complexity.
Accuracy and the resources consumption achieved
Suitable for real-time applications.
16

## Slide 18: References
[1] Global Agenda Council on Ageing Society, World Economic Forum,Global Population Ageing : Peril or Promise?, 2011.
[2] D. P. Morales, A. García, E. Castillo, M. A. Carvajal, J. Banqueri, and A. J. Palma, “Flexible ECG acquisition system based on analog and digital reconfigurable devices”, Sensors and Actuators A Phys., vol.165, no. 2, pp. 261-270, 2011.
[3] N. Van Helleputte, J. M. Tomasik, W. Galjan, A. Mora-Sánchez, D.Schroeder, W. H. Krautschneider, and R. Puers, “A flexible systemon-chip (SoC) for biomedical signal acquisition and processing”,Sensors and Actuators A Phys., vol. 142, no. 1, pp.361-368, 2008.
[4] H. Kim, S. Kim, N. Van Helleputte, A. Artes, M. Konijnenburg, J.Huisken, C. Van Hoof, and R. F. Yazicioglu, “A configurable
And low-power mixed signal SoC for portable ECG monitoring applications”, IEEE Trans. on Biomedical Circuits and Systems, vol.8, no. 2, pp. 257-267, 2014.
[5] G. G. Berntson, J. Thomas Bigger, D. L. Eckberg, P. Grossman, P.Kaufmann, M. Malik, H. N. Nagaraja, S. W. Porges, J. P. Saul, P. H.Stone, and M. W. Der Molen, “Heart rate variability: Origins,methods, and interpretive caveats”, Psychophysiology, vol. 34, no. 6,pp. 623-648, 1997.
[6] G. M. Friesen, T. C. Jannett, M. a Jadallah, S. L. Yates, S. R. Quint,and H. T. Nagle, “A comparison of the noise sensitivity of nine QRS detection algorithms”, IEEE Trans. on Biomedical Engineering, vol.37, no. 1, pp. 85-98, 1990.
[7] J. Lee and G. Lee, “Design of an Adaptive Filter with a Dynamic Structure for ECG Signal Processing”, International Journal of Control Automation and Systems, vol. 3, no. 1, pp. 137-142, 2005.

## Slide 19: Thank You